## Slide 1: LLM-Driven Schematic Generation for STMicroelectronics Components in KiCAD.v7
Mentor: Mr. Saurabh Rawat
Mentee: Dushyant Singh
June 2026

## Slide 2
LLM Driven End to End PCB Generation for KiCAD
LLM-Driven End-to-End PCB Generation for STMicroelectronics
From a natural-language circuit spec → ERC-validated SKiDL netlist → native KiCad 9 schematic → automated placement & routing.
Grounded in ST datasheets and ST design guidelines, targeting ST component families.
Supervised first-draft today; trajectory toward full end-to-end automation before fabrication.
Aim
Automate the full path from a natural-language spec to a placed, routed, fabrication-ready PCB for ST parts — end to end, not just the schematic.
Method
PCBSchemaGen: LLM + RAG over ST datasheets → SKiDL netlist → native KiCad 9 schematic → auto-placement → Freerouting routing.
Result
0 ERC errors with correct footprints on two ST benchmarks (I2C & SPI). ST-style power auto-wiring in progress; layout + routing next.
End-to-End Pipeline
Natural-Language Prompt
LLM + RAG (ST datasheets)
SKiDL Netlist — ERC ✓
KiCad 9 Schematic — 0 ERC ✓
Auto-Placement + Routing
Fabrication-Ready PCB
Built
In progress

## Slide 3
3
Pipeline Flowchart End-to-End
Text + ST Part Numbers
Retrieves datasheet chunks via ChromaDB
Part(), Net(), += SKiDL syntax
Runs ERC — catches electrical violations
stm32_mvc.net skidl_REPL.svg

## Slide 4
The Problem — What Engineers Waste Time On
Why schematic entry for STM32 designs is slow and error-prone
Pain 1
Pin lookup: engineers manually search datasheets for every alternate function mapping on STM32
Pain 2
Repetition: same reset circuit, boot pin, decoupling caps — redrawn from scratch every board
Pain 3
Silent errors: wrong STM32 AF pin won't fail ERC — only fails on physical hardware
Pain 4
Scale: full STM32 application board has 150-300 components — manual entry takes days

## Slide 5
What We Used
Framework
PCBSchemaGen
arXiv:2602.00510
Code Gen
SKiDL
Python Library
LLM
Qwen2.5-coder:7b
via Ollama (local)
RAG
ChromaDB +
sentence-transformers
Compute
Lightning AI
Ubuntu 24.04 GPU
Research
Framework
Used as
base pipeline
Generates
KiCad Netlists
From Python
circuit code
Local inference
No API cost
GPU accelerated
on Lightning AI
338 chunks
STM32F411CE PDF
Locally embedded
no cloud needed
Ubuntu 24.04
15GB RAM
T4 GPU
for inference
KiCad 7
Netlist + SVG
Output
SKiDL ERC
Electrical
Rule Check
ChromaDB
Vector Store
Persistent
Ollama
Local Model
Runner
netlistsvg
SVG Schematic
Renderer

## Slide 6
Environment Setup — Challenges and Fixes
Getting the pipeline running — challenges and fixes
pcbnew import
Fixed: Used Linux (WSL2/Lightning AI) — pcbnew importable only on Linux, not Windows
Library paths
Fixed: Injected repo library path into SKiDL search paths inside subprocess
Script errors
Fixed: Removed stray code and duplicate injection headers causing NameError
netlistsvg
Fixed: Installed Node.js and netlistsvg via npm for SVG schematic output
Ubuntu 24.04
Fixed: KiCad 9 PPA not available — KiCad 7 confirmed fully compatible with repo

## Slide 7
Sample Test Results — 17/17 Passing
Proof of working infrastructure — all 17 sample design tests passing
Result
17 / 17 sample tasks PASS
Tasks span digital, analog, and power circuit types
Voltage dividers, LDO regulators, half-bridge gate drivers,
isolated amplifiers, synchronous buck converters,
and full 3-phase inverter designs
All passing before any LLM call is made —
confirms pipeline infrastructure is solid

## Slide 8
LLM Models Comparison
Model
Syntax
Correct
Task
Following
Topology
Pass
Speed
on CPU
Verdict
Qwen2.5-
coder:3b
✗ Wrong
syntax
✗ Ignores
task
✗ FAIL
Fast
Too small
for SKiDL
Qwen2.5-
coder:7b
✓ Correct
SKiDL
Partial
(Task 1 ok)
Partial
(Task 1 only)
Medium
Good for
simple circuits
Qwen3:8b
✓ Correct
SKiDL
Better
(thinking mode)
Task 1
passes GPU
Slow CPU
Fast GPU
Best local
option
Claude Sonnet
(API)
✓ Perfect
SKiDL
✓ Full
compliance
✓ Expected
full pass
Fast
(API)
Recommended
for production
Key finding: SKiDL syntax is solved by 7B+ models. Complex IC reasoning needs frontier LLM or strong RAG grounding.

## Slide 9
RAG System — The Brain
1
Download STM32F411CE PDF
2
Extract text with PyMuPDF
3
Chunk at ~800 tokens each
4
Embed with sentence-transformers
(all-MiniLM-L6-v2, runs locally)
5
Store in ChromaDB — query at
generation time, top-4 chunks
injected into LLM prompt
Datasheet Processed
338
Chunks
~800
tokens each
Query Results (verified retrieval)
NRST query →
Retrieved reset
circuit specs
BOOT0 query →
Pin 24 table
boot modes
Model: all-MiniLM-L6-v2 | DB: ChromaDB | No cloud, no API key needed

## Slide 10
Adding STM32 Components to the Pipeline
The repo shipped with zero ST components — we built the entire ST integration from scratch
KiCad Symbol
Defined 48-pin STM32F411CEU6 in test.kicad_sym — rectangular body, pins distributed on both sides
Knowledge Graph
Added pin roles to kg.json: VBAT=supply_vdd, NRST=logic_in, BOOT0=logic_in, VDD=supply_vdd, VSS=supply_gnd
Constraints
Topological rules: 100nF cap on every VDD pin, 100nF on NRST to GND, 10k pull-down on BOOT0
Benchmark Task
Wrote new task: STM32F411CEU6 minimum viable circuit — power, reset, boot pins

## Slide 11
11
The Natural Language Prompt Given for this Circuit

## Slide 12
Generated SKiDL Code
Actual LLM-generated SKiDL code — validated by ERC
Input
Natural language: STM32F411CEU6 minimum viable circuit
RAG
Retrieved: NRST 100nF, BOOT0 pull-down, VDD decoupling rules
Output
Part(), Net(), += connections — correct SKiDL syntax
ERC
0 errors, 45 warnings (all expected — unconnected GPIO pins)

## Slide 13
Key Result — STM32 Circuit Generated
First ST-only circuit — generated, validated, zero ERC errors
MCU
STM32F411CEU6 (48-pin UFQFPN)
C1-C5
100nF decoupling on VBAT, VDDA, VDD x2, NRST
R1
10k pull-down on BOOT0 (flash boot mode)
ERC
0 errors | 45 warnings (expected)
Files
stm32f411_mvc.net (7.2KB) + skidl_REPL.svg (50KB)

## Slide 14
14
What it looks in KiCAD.v9

## Slide 15
ERC Validation and Output Files
ERC validation — the pipeline self-checks electrical correctness
0 Errors
Zero electrical rule violations in the generated netlist
45 Warnings
All expected — unconnected GPIO pins (intentional in MVC) + missing power flags
Netlist
stm32f411_mvc.net — 7.2KB KiCad-compatible netlist file
SVG
skidl_REPL.svg — 50KB schematic visualization with rectangular IC body
Verified on
Lightning AI — Ubuntu 24.04, KiCad 7, Python 3.12

## Slide 16
Approach Comparison
Method
KiCad
Output
OrCAD /
Allegro
ST Component
Fit
Cost
Status
PCBSchemaGen
+ SKiDL
Direct
Netlist
Via EDIF
(manual)
Strong
with RAG
Low
(local)
USED ✓
KiCad
MCP Server
Direct
manipulation
None
Promising
None
Phase 1
target
kicad-sch-api
Native
.kicad_sch
None
Good
None
Alternative
Atopile
Direct
Netlist
Exportable
Good
(Claude gen)
None
Future
Flux.ai
Export
Export
Unknown
High
($$)
Commercial
only
CELUS
None
Altium only
Component
focus
High
($$)
Not
relevant

## Slide 17
Limitations and Roadmap
Model ceiling
7B model ignores complex ICs.
Frontier LLM (Claude Sonnet) needed for production.
ST library gap
Only STM32F411CEU6 added.
Full ST portfolio needs KG encoding.
KiCad only
No OrCAD/Allegro direct path.
EDIF workaround needs manual remapping.
Scale limit
150-300 component boards need
hierarchical generation — not yet built.
Phase 1
DONE ✓
Pipeline running
17/17 tests pass
1st ST circuit — 0 ERC errors
Phase 2
NEXT
Claude Sonnet API
Full STM32F4 KG
ST benchmark tasks
Phase 3
FUTURE
Hierarchical generation
Simulation-in-loop
OrCAD MCP integration

## Slide 18
Conclusion
What this project demonstrates
Proven
End-to-end pipeline works: natural language to KiCad netlist with 0 ERC errors on ST components
Built
RAG system over ST datasheets + STM32 KG + SKiDL + local LLM — all running on Lightning AI
Next step
Connect Claude Sonnet API — same infrastructure, dramatically better complex circuit quality
Vision
A fully ST-aware schematic generation system — engineer describes intent, pipeline draws it

## Slide 19
Execution Environment
Execution environment
Platform
Lightning AI Studio — cloud Linux
OS
Ubuntu 24.04.4 LTS
RAM
15GB total, 13GB available
GPU
T4 GPU for Qwen3:8b inference
Python
3.12.11 + KiCad 7.0.11 + Ollama